## Slide 1: Quality Control for Sequencing Experiments
v2023-04
Simon Andrews, Sarah Inglesfield
simon.andrews@babraham.ac.uk
sarah.inglesfield@babraham.ac.uk

## Slide 2
Support service for bioinformatics
  Academic – Babraham Institute
  Commercial – Consultancy
Support BI Sequencing Facility
  MiSeq/ HiSeq/ NextSeq-based sequencing service
  Data Management / Processing / Analysis

## Slide 3: Interests in QC
QC packages
Application specific QC
Data visualisation QC
Notes: Developed QC for in-house sequencing
Developed QC packages
  FastQC
  BamQC
  FastQ Screen
Developed application specific QC
  Bismark (bisulphite methylation)
  HiCUP (Hi-C genome structure)
Developed data visualisation QC
  SeqMonk (generic sequencing visualisation / analysis)
    RNA-Seq QC
    Small RNA QC
    Duplication QC

## Slide 4: An example of why QC is important…
Single Cell RNA-Seq
  Each dot is a cell
  An outgroup is clearly visible
  What is it?
PC1
PC2

## Slide 5: Genes for PC2 (85 total)
Gene Description
Arhgef4 Rho guanine nucleotide exchange factor (GEF) 4
Cflar CASP8 and FADD-like apoptosis regulator
Als2 amyotrophic lateral sclerosis 2 (juvenile) homolog (human)
Cxcr2 chemokine (C-X-C motif) receptor 2
Col4a3 collagen, type IV, alpha 3
Sag retinal S-antigen
Gpr35 G protein-coupled receptor 35
Acmsd amino carboxymuconate semialdehyde decarboxylase
Qsox1 quiescin Q6 sulfhydryl oxidase 1
9430070O13Rik RIKEN cDNA 9430070O13 gene
Mrps14 mitochondrial ribosomal protein S14
Scyl3 SCY1-like 3 (S. cerevisiae)
Ildr2 immunoglobulin-like domain containing receptor 2
Atp1a2 ATPase, Na+/K+ transporting, alpha 2 polypeptide
Slamf8 SLAM family member 8
Wdr38 WD repeat domain 38
Exd1 exonuclease 3'-5' domain containing 1
Serf2 small EDRK-rich factor 2

## Slide 6: Coverage of Raw Data
Normal Gene
PCA Gene

## Slide 7: Using a different read mapper…
Conclusion: The separation in the original graph was a technical artefact of no biological interest. If we'd published this it would have mislead others. Even if we find it we've wasted some time and effort.
PC1
PC2

## Slide 8: What is the point of QC?
Technical problems don't cause pipelines to fail
Technical problems don't prevent hits being generated
Technical hits often look biologically real
Unexpected, interesting effects can easily be missed
Finding problems through follow-on work is slow and expensive!
QC saves you time and effort! (and money)

## Slide 9: Course Structure
How does Illumina Sequencing work?
What can QC tell us?
  QC Software
  Universal metrics
  Library Dependent metrics
  Consistency
Putting QC into Practice

## Slide 10: How Does Illumina Sequencing Work?

## Slide 11: Illumina Sequencing: An Overview
Library Generation
Attach to Flow Cell
DNAP
Sequence by Synthesis (SBS)
Sequencing Reads

## Slide 12
Fridge
Pumps
Microscope
Compartment

## Slide 13
Flow Cell

## Slide 14: Illumina Sequencing: An Overview
Attach to Flow Cell
DNAP
Library Generation
Sequence by Synthesis (SBS)
Sequencing Reads

## Slide 15: SBS For a Single Molecule
G A T T C A G
A
G
T
C

## Slide 16: SBS For a Single Molecule
C
G A T T C A G

## Slide 17: SBS For a Single Molecule
C
G A T T C A G
A
G
T
C
1 Cycle

## Slide 18: SBS For a Single Molecule
C
G A T T C A G
G
A
T
A
T
C
2 Cycles
3 Cycles
4 Cycles
5 Cycles
6 Cycles
7 Cycles
... Read length
ect...

## Slide 19: Comparing Chemistry
A
T
C
G
4 Channel Chemistry
A
G
T
C
2 Channel Chemistry
A
G
T
C
A
G
C
T
1 Channel Chemistry
Signal
Image
Base Call
Notes: 1 channel chemistry isn’t very common – used by the iSeq™ 100 System

## Slide 20: Comparing Chemistry
4 Channel |  |  | 
T | C | A | G
2 Channel |  |  |  | 
T | C | A |  | G
1 Channel |  |  | 
T | C | A | G
No Signal is interpreted as G
Signal
Image
Base Call

## Slide 21
Detecting a Signal
One Molecule isn’t Enough
Amplify to generate Cluster
Cycle 1
Cycle 2
Cycle 3
Multiple Clusters on a Flow Cell

## Slide 22: Flow Cell Imaging
Glass Slide
Image
Image
Flow in
Flow out
Tiles
Lanes
Swaths
Flow Cell

## Slide 23: Real Illumina Sequence Data

## Slide 24
Non Patterned Flow Cell
Patterned Flow Cell
Random Clusters
Creating Clusters
Pre-defined Clusters
Notes: Flow cell is coated with a lawn of oligo primers complementary to adapter region of fragment strand
Patterned allows greater density

## Slide 25: Creating Clusters: Patterned Flow Cells
Single molecule attaches in a nano well
Recombinase Polymerase
Bridge Amplification
Cluster of identical (ish) molecules created in a nanowell
Amplification is faster than seeding
Notes: Key difference is the flow cell and the chemistry
Rather than a random lawn of primers the primers are located in nanowells – can be more densely packed
Then the actual amplification is slightly different – uses what Illumina term Exclusion amplification chemistry
  Essentially Recombinase Polymerase Amplification – allows amplification to proceed without thermal/chemical melting
  This amplification is quick and faster than the seeding rate
    In part because seeding is controlled by electric field which also helps direct molecules to wells
So overall very similar and this is the approach of newer sequencers
Limited density less data
http://enseqlopedia.com/2016/12/index-mis-assignment-between-samples-on-hiseq-4000-and-x-ten/

## Slide 26: Good and Bad things about clusters
Good
Generates large signal
Is robust to random mistakes
Needs a small amount of starting material
Bad
Bridging limits length
Molecules in a cluster get out of sync
  2 bases added
  No bases added
  Reaction stalls
Can get mixed signals if clusters overlap (non-patterned)
Can get re-seeding (patterned)
Can get index hopping (patterned)

## Slide 27: Different sequencers, same chemistry
Sequencer | Number of lanes | Reads per lane | Max read length | Dyes
iSeq 100 | 1 | ~4 million | 150bp | 1
MiniSeq | 1 | ~7 million | 150bp | 2
MiSeq | 1 | ~20 million | 300bp | 4
NextSeq | 1 | ~400 million | 150bp | 2
HiSeq 2xxx | 16 | ~200 million | 150bp | 4
HiSeq 4xxx | 16 | ~300 million | 150bp | 4
NovaSeq | 8 | ~2.5 billion | 150bp | 2

## Slide 28: Illumina Sequencing: An Overview
Attach to Flow Cell
DNAP
Library Generation
Sequence by Synthesis (SBS)
Sequencing Reads

## Slide 29: What Reads Do You Get
Insert
Adapter
Barcode
Adapter
Barcode
Insert
Adapter
Primer
Read 1
Insert
Adapter
Primer
Read 2
Barcode Read
Single End Run
(one fastq file)
Paired End Run
(two fastq files)
Used to separate libraries – often don't see the fastq file

## Slide 30: FastQ Format Data
@HWUSI-EAS611:34:6669YAAXX:1:1:5069:1159 1:N:0:
TCGATAATACCGTTTTTTTCCGTTTGATGTTGATACCATT
+
IIHIIHIIIIIIIIIIIIIIIIIIIIIIIHIIIIHIIIII
@HWUSI-EAS611:34:6669YAAXX:1:1:5243:1158 1:N:0:
TATCTGTAGATTTCACAGACTCAAATGTAAATATGCAGAG
+
DF=DBD<BBFGGGGGGGBD@GGGD4@CA3CGG>DDD:D,B
@HWUSI-EAS611:34:6669YAAXX:1:1:5266:1162 1:N:0:
GGAGGAAGTATCACTTCCTTGCCTGCCTCCTCTGGGGCCT
+
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG

## Slide 31: A single FastQ Entry
Header - starts with @
Base calls (can include N or IUPAC codes)
Mid-line - starts with + usually empty
Quality scores (= Phred Scores)
@HWUSI-EAS611:34:6669YAAXX:1:1:5266:1162 1:N:0:
GGAGGAAGTATCACTTCCTTGCCTGCCTCCTCTGGGGCCT
+
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG
Notes:   Must start with a unique identifier (up to first space)
  Can often have substructure
  Per base signal:noise assessment
  ASCII encoded Phred score

## Slide 32: Illumina Header Sections
Starts with @ (required by fastq spec)
Instrument ID (HWUSI-EAS611)
Run number (34)
Flowcell ID (6669YAAXX)
Lane (5)
Tile (1)
X-position (5069)
Y-position (1159)
[space]
Read number (1)
Was filtered (Y/N) (N) - You wouldn't normally see the Ys
Control number (0 = no control)
Sample number (only if demultiplexed using Illumina's software)
@HWUSI-EAS611:34:6669YAAXX:5:1:5069:1159 1:N:0:

## Slide 33: Phred Scores
Start from (p) - the probability that the reported call is incorrect
Initial transformation to a Phred score - positive integer from floating point
Phred = -10 * (int)log10(p)
    p=0.1 Phred = 10
    p=0.01 Phred = 20
    p=0.001 Phred = 30

## Slide 34: Phred Score Encoding
Translation of Phred score to single ASCII letter
Based on standard ASCII table
Can't translate directly
  low values are non-printing
Encode with Sanger System*
  Phred+33
  *Historically also had Illumina = Phred+64

## Slide 35: Phred score encoding
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG
: = ASCII 58
Phred33 encoding so Phred = 25
p = 10^(25/-10)
p = 0.003

## Slide 36: Phred score encoding
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG
BETTER
WORSE
or
Symbol | ASCII | Phred | Probability of miscall
: | 58 | 25 | p = 10^(25/-10) = 0.003
G | 71 | ? | ?

## Slide 37: Phred score encoding
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG
BETTER
Symbol | ASCII | Phred | Probability of miscall
: | 58 | 25 | p = 10^(25/-10) = 0.003
G | 71 | 38 | p = 10^(38/-10) = 0.00016

## Slide 38: Phred score encoding
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG
Symbol | ASCII | Phred | Probability of miscall
G | 71 | 38 | p = 10^(38/-10) = 0.00016
B | 66 | ? | ?
BETTER
WORSE
or

## Slide 39: Phred score encoding
:GBGGGGGGGGGDGGDEDGGDGGGGDHHDHGHHGBGG:GG
Symbol | ASCII | Phred | Probability of miscall
G | 71 | 38 | p = 10^(38/-10) = 0.00016
B | 66 | 33 | p = 10^(33/-10) = 0.0005
WORSE

## Slide 40: Aligned Data – BAM files
Expanded file containing alignment data as well as everything in the fastq file
Two sections
  Header (list of reference seqs and how the file was created)
  Alignments (details of the alignments and sequences)
Need special programs to read, normally 'samtools'

## Slide 41: BAM Header
[andrewss@headstone Sample_lane1]$ samtools view -H lane1000_TTAGGC_test_L001_R1_GRCm38_hisat2.bam
@HD VN:1.0 SO:unsorted
@SQ SN:1 LN:195471971
@SQ SN:10 LN:130694993
@SQ SN:11 LN:122082543
@SQ SN:12 LN:120129022
@SQ SN:13 LN:120421639
…etc…
@PG ID:hisat2 PN:hisat2 VN:2.1.0 CL:"/bi/apps/hisat2/2.1.0/hisat2-align-s --wrapper basic-0 --dta --sp 1000,1000 -p 7 -t --phred33-quals -x /bi/scratch/Genomes/Mouse/GRCm38/Mus_musculus.GRCm38 --known-splicesite-infile /bi/scratch/Genomes/Mouse/GRCm38/Mus_musculus.GRCm38.90.hisat2_splices.txt -U /tmp/17469.unp"

## Slide 42: BAM Alignments
Sections
  Sequence name HWI-D00436:394:CBGLBANXX:1:1101:1222:1861
  Alignment Flags 16
  Reference sequence name chr18
  Start position 5794485
  Mapping Quality (Phred) 60
  Alignment (CIGAR) string 50M
  Paired sequence name *
  Paired sequence position 0
  Total insert length 0
  Called Bases AAAAGATCTCTTGATTTAGAATTTTCTCTCAAATGTGAGGGACTTTTATN
  Base Quality String (Phred 33) GGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGBA<=#
  Other Tags
[andrewss@headstone Sample_lane1]$ samtools view lane6045_TTAGGC_Col4_contr_L001_R1_trimmed_GRCm38_hisat2.bam | less
HWI-D00436:394:CBGLBANXX:1:1101:1222:1861 16 chr18 57944851 60 50M * 0 0 AAAAGATCTCTTGATTTAGAATTTTCTCTCAAATGTGAGGGACTTTTATN GGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGGBA<=# AS:i:-2 XN:i:0 XM:i:1 XO:i:0 XG:i:0 NM:i:1 MD:Z:49G0 YT:Z:UU NH:i:1

## Slide 43: BAM Flags
A 12-bit binary number with a set of TRUE/FALSE values
  Sequence is paired end
  All reads from this template are aligned
  This read didn't align
  The paired read didn't align
  The read aligned in the reverse orientation
  The paired read aligned in the reverse orientiation
  This is the first read
  This is the second read
  This is not the best alignment for this read
  This read failed upstream QC
  This read is a duplicate
  This is part of a chimeric alignment
https://broadinstitute.github.io/picard/explain-flags.html

## Slide 44: What can QC tell us?

## Slide 45: QC metrics can we work with
Per Base Quality Scores
Library composition
  Base level
  Sequence Level
  Known sequences
Mapping statistics
Downstream Quantitation Values

## Slide 46: Context is Key for QC
QC should be about what you expect and what you see
Expectations
Observations
Critical Analysis
Understanding & Confidence
Notes: Therefore some aspects of QC are highly context dependent

## Slide 47: Context is Key for QC
Expectations
Universal
Library Dependent
Consistency
Individual Library:
Replicate Libraries:

## Slide 48: Some Software Packages for Sequence QC

## Slide 49: FastQC
Reads raw fastq files
Performs multiple checks
  Pass/warn/fail
  Compares to genomic library
HTML Report
https://www.bioinformatics.babraham.ac.uk/projects/fastqc/

## Slide 50: FastQ Screen
Reads fastq files
Maps against a range of species / contaminants
Identifies unexpected sequences in your library
https://www.bioinformatics.babraham.ac.uk/projects/fastq_screen/

## Slide 51: Librarian
Reads FastQ files
Looks at the base composition
Predict library type
Under development
https://github.com/DesmondWillowbrook/Librarian

## Slide 52: MultiQC
Aggregates QC information from multiple samples
Large number of programs supported
Combined HTML report
https://multiqc.info/

## Slide 53: Assessing Universal Metrics

## Slide 54: Universal QC Metrics
Demultiplexing
Base Call Quality
Adapter Content
Mapping Quality

## Slide 55: Demultiplexing: Barcode Sequences
Insert
Adapter
Adapter
Barcode
Barcode

## Slide 56: Demultiplexing: Barcode Sequences

## Slide 57: Demultiplexing: Barcode Sequences

## Slide 58: Demultiplexing: Barcode Sequences

## Slide 59: Base Call Qualities – Per Cycle
Read Position / Cycles of Chemistry
Phred Score

## Slide 60: Base Call Qualities – Per Cycle
Read Position / Cycles of Chemistry
Phred Score

## Slide 61: Base Call Qualities – Per Cycle

## Slide 62: Diagnosing Poor Base Call Qualities
Not everything is bad
Can see identify why some parts are bad and others aren't?
May help to fix future runs

## Slide 63: Per-Read Quality
Are all reads equally affected?
Is there a subset of reads which are always poor whilst others are good?

## Slide 64: Positional Quality
Lanes
Tiles
Top
Bottom
Random Patterning
Position Specific
Patterning

## Slide 65: Positional Quality

## Slide 66: Read-through Adapters
Insert
Adapter
Adapter
Primer
Read 1
Insert
Adapter
Adapter
Primer
Read 1

## Slide 67: Measuring Read-though Adapters
Insert
Adapter
Adapter
Primer
Read 1

## Slide 68: Clean-Up Options
Some quality issues may need to also remove specific reads
Trimming 3’ end:
Remove adapter read through
Remove poor quality bases
Despite issues may still be good enough for what is needed e.g. mapping
Insert
Adapter
Adapter
Primer
Read 1

## Slide 69: Mapping Statistics
Time loading forward index: 00:01:10
Time loading reference: 00:00:05
Multiseed full-index search: 00:20:47
24548251 reads; of these:
24548251 (100.00%) were paired; of these:
1472534 (6.00%) aligned concordantly 0 times
21491188 (87.55%) aligned concordantly exactly 1 time
1584529 (6.45%) aligned concordantly >1 times
94.00% overall alignment rate
Time searching: 00:20:52
Overall time: 00:22:02
If many reads do not map to the expected genome…
…Where do they come from?

## Slide 70: Library Screening
Map your reads against a range of reference genomes
Classify matches as: unique to one species & single or multiple mapping
Notes:   Any species you normally work with
  Common lab contaminants (E coli and Human)
  Artificial sequences (adapters, vectors)
  Known problematic sequences (rRNA)

## Slide 71: Library Screening

## Slide 72: Library Screening

## Slide 73: Library Screening

## Slide 74: Assessing Library Dependent Metrics

## Slide 75: Library Dependent QC Metrics
FastQC expects a Genomic Library: Do you?
GC Content
Base Composition
Duplication
Concern or Expected?
Some QC metrics will be influenced by what you are sequencing
Notes: FastQC was built for standard genomic libraries, therefore it expects a standard genomic library
You Might not!

## Slide 76: Library GC Content
Generic summary of library composition at a read level
Expect a normally distributed set of values centred on the overall GC content
Notes: SRR14760809_GSM5363752_ATAC-seq_Tet1_KO_Replicate_#3_Mus_musculus_ATAC-seq_1.fastq.gz

## Slide 77: Sharp Peaks in GC
Specific Contamination with single sequence or closely related sequences
Artificial sequences, ribosomal RNA, contaminants
Concern or Expected
Notes: file:///C:/Users/inglesfs/Downloads/SRR2089635_GSM1811753_WT_MII_oocyte_1_RNA-seq_Mus_musculus_RNA-Seq_2_val_2_fastqc.html#M5
(alternative single peak enriched with GC from: file:///C:/Users/inglesfs/Downloads/SRR6491539_GSM2891677_prpa_TOP1_INP_2_1_Homo_sapiens_ChIP-Seq_1_fastqc.html#M5)
From Masui_2023 file:///C:/Users/inglesfs/Downloads/SRR18752205_GSM6043804_Control_Eed_EPC._rep2_Mus_musculus_RNA-Seq_1_fastqc.html#M9
(looking at total RNA so ribosomal material makes sense here!)

## Slide 78
Drosophila
Mouse
Broader Peaks in GC
H3K4me1 ChIP: enrich for regions rich in GC
More extensive mixture of reads with different GC content
Concern or Expected
Notes: Sample 4777 Sierra
lane2_Ub119_58_TCCGTCTT_L002_3536STDY7827645_R1_trimmed.fq.gz
Mouse sample with a drosophila spike-in (only around 1.5%)
Right: Feeney_2016 SRR3217295_GSM2084579_H3K4me1_pre-B_ChIP-seq_Mus_musculus_ChIP-Seq_trimmed.fq.gz

## Slide 79
More extensive subset of reads with extreme differences in GC
PolyG’s
GC Skew
PolyA’s
Concern or Expected
Notes: Left
file:///C:/Users/inglesfs/Downloads/SRR2240620_GSM1868818_EPI4.1_Homo_sapiens_RNA-Seq_1_val_1_fastqc%20(1).html#M5
(alternatives: file:///C:/Users/inglesfs/Downloads/SRR5476919_GSM2587220_E7.0_ExE_rep2_RNA_Mus_musculus_RNA-Seq_1_fastqc.html#M5)
Right This is an example of artificial GC enrichment due to polyG sequences
FromDorighi_2017 SRR5466763_GSM2586555_Input_DNA_WT_Mus_musculus_ChIP-Seq_1_trimmed.fq.gz

## Slide 80: Library Base Composition
For every chemistry cycle we can look at the number of ATGC we call
For Libraries with random start positions the composition should be the same for all cycles
Notes: Balance between GATC can vary
  GC content of the species (GC separates from AT)
  Systematic biases per library type
GC separate to AT
Lines mostly flat
So if you don’t see this can indicate some biases in the sequences you get back, but is that inherently a bad thing – well it depends on what you see vs what you expect
file:///C:/Users/inglesfs/Downloads/arrest_M-CDK_inhibited_rep6_SRR7533474_1_fastqc.html#M4

## Slide 81: Bias Composition Throughout
Very low diversity
Proportional biases of bases at specific positions:
Concern or Expected
Amplicon
Wrong Sequence
Notes: Left: Sample 5891 CRISPRa_gRNA_plasmid_library – technical error, sequenced primer before the variable sequence
Right: Sample 4135 lineage Cas9 4days Nextera amplicon
https://www.bioinformatics.babraham.ac.uk/sierra/sierra.pl/lane5716_AGGCAGAA_AAGGAGTA_E03_L001_R1_val_1_fastqc.html?action=send_file&lane_id=5716&path=%2Fdata%2Fprivate%2Fsierra%2Fdata%2F170802_M02293_0292_000000000-AU96R%2FUnaligned%2FProject_000000000-AU96R%2FSample_lane1%2Flane5716_AGGCAGAA_AAGGAGTA_E03_L001_R1_val_1_fastqc.html#M4

## Slide 82: Bias Composition Throughout
Consistent disproportional expression of bases
Concern or Expected
WGBS
Notes: http://bioinfdev.babraham.ac.uk/labrador/download_file.php?fn=Guo_2014/QC/SRR1295942_WGBS_human_ICM_lane1_1_val_1_fastqc.html

## Slide 83: Bias Composition at 5’ end
Proportional biases of bases at the start of a read: A preferred start site
RRBS – Restriction Start Site
ATAC – Transposases
Concern or Expected
Notes: ATAC: file:///C:/Users/inglesfs/Downloads/SRR10347760_GSM4140579_MuSC_d0_Young_bulkATACseq_Rep2_Mus_musculus_ATAC-seq_1_fastqc.html#M4
RRBS: file:///C:/Users/inglesfs/Downloads/SRR1544466_RRBS_E7_5_1_val_1_fastqc.html#M4

## Slide 84: Bias Composition at 3’ end
Proportional biases of bases at the end of a read: consistent closing sequence
Concern or Expected
Notes: https://www.bioinformatics.babraham.ac.uk/sierra/sierra.pl/lane8413_ATGAGC_2-JH1724-Log_L001_R1_fastqc.html?action=send_file&lane_id=8413&path=%2Fdata%2Fprivate%2Fsierra%2Fdata%2F230306_NB501547_0028_AHGLMTBGXM%2FUnaligned%2FProject_NextSeq%2FSample_lane1%2Flane8413_ATGAGC_2-JH1724-Log_L001_R1_fastqc.html#M4
lane8413_ATGAGC_2-JH1724-Log_L001_R1_fastqc.html

## Slide 85
Bias Composition at 3’ end
Concern or Expected
Proportional biases of bases at the end of a read: consistent closing sequence
Bioinformatics processing can also influence QC metrics!
Notes: https://www.bioinformatics.babraham.ac.uk/sierra/sierra.pl/lane8413_ATGAGC_2-JH1724-Log_L001_R1_trimmed_fastqc.html?action=send_file&lane_id=8413&path=%2Fdata%2Fprivate%2Fsierra%2Fdata%2F230306_NB501547_0028_AHGLMTBGXM%2FUnaligned%2FProject_NextSeq%2FSample_lane1%2Flane8413_ATGAGC_2-JH1724-Log_L001_R1_trimmed_fastqc.html#M4

## Slide 86: Duplication
How frequently the exact same sequence appears in your library
For WGS expect most sequences to be unique

## Slide 87: Duplication
If the exact same sequence appears more than once it could be…
ATCCGAGCTATTCGGCGAGCTCGCCAGTTACG
ATCCGAGCTATTCGGCGAGCTCGCCAGTTACG
ATCCGAGCTATTCGGCGAGCTCGCCAGTTACG
Technical:
ATCCGAGCTATTCGGCGAGCTCGCCAGTTACG
ATCCGAGCTATTCGGCGAGCTCGCCAGTTACG
ATCCGAGCTATTCGGCGAGCTCGCCAGTTACG
Coincidental:
Deep sequencing
Highly present sequences
Restricted diversity libraries
PCR duplicates
Notes:   The sequences come from different biological molecules and the duplication is coincidental
    Deep sequencing
    Highly present sequences (repeats for example)
    Restricted diversity libraries (amplicon sequencing, restricted libraries)
  The sequences come from the same biological and the duplication is technical
    PCR duplicates

## Slide 88: Duplication
BUT could have technical duplication with expected coincidental duplication!
RNA-Seq
Amplicon
Concern or Expected
Notes:   Some Libraries we expect coincidental duplication….
  Modest duplication: RNAseq - file:///C:/Users/inglesfs/Downloads/SRR14760800_GSM5363743_RNA-seq_Tet1_KO_Replicate_R3_Mus_musculus_RNA-Seq_1_val_1_fastqc.html#M8
  Extreme duplication: Amplicon Bisulphite seq - https://www.bioinformatics.babraham.ac.uk/sierra/sierra.pl/UHRF1chr1_L001_R2_val_2_fastqc.html?action=send_file&lane_id=8398&path=%2Fdata%2Fprivate%2Fsierra%2Fdata%2F230214_M02293_0001_AMPLICONBS%2FUnaligned%2FProject_Sanger%2FSample_lane1%2FUHRF1chr1_L001_R2_val_2_fastqc.html#M8

## Slide 89: Overrepresented Sequences
Extreme duplication
The exact same sequence is a significant proportion of the whole library (which might not be duplicated overall)
Poly Sequences
Specific Sequences
Notes: Normally comes from artificial sequences (primers, adapters, vectors etc)
Can search a database of known sequences to find matches

## Slide 90: Sources of Poly Sequences
  PolyN – Quality too poor to make any calls
  PolyG – Empty space in 2 colour chemistry, can be technically “high quality” calls
Notes: PolyN = Xie_2013_2 SRR304956_Reference_Epigenome_ChIP-Seq_Analysis_of_H3K27ac_in_BMP4_Trophoblast_Cells_1.fastq.gz
PolyG = Dorighi_2017 SRR5466763_GSM2586555_Input_DNA_WT_Mus_musculus_ChIP-Seq_1_trimmed.fq.gz

## Slide 91: Sources of Poly Sequences
  PolyA (or PolyT) – Common in RNA-Seq
Notes: From http://bioinfdev.babraham.ac.uk/labrador/download_file.php?fn=Blakeley_2015/QC/SRR2240620_GSM1868818_EPI4.1_Homo_sapiens_RNA-Seq_1_val_1_fastqc.html
(alternative: file:///C:/Users/inglesfs/Downloads/SRR3337287_2-cell_embryo_RNA-seq_20cells_rep2_1_fastqc.html#M9)
Jiang_2023 file:///C:/Users/inglesfs/Downloads/SRR12439945_GSM4725073_mouse_placental_cells_E09.5_Mus_musculus_RNA-Seq_2_fastqc.html#M10

## Slide 92: Overrepresented Specific Sequences
Normally artificial sequences (primers, adapters, vectors etc)
Can search a database of known sequences to find matches
Insert
Adapter
Adapter
Barcode
Barcode
Adapter
Adapter
Barcode
Barcode
Example of an Adapter dimer:

## Slide 93: Overrepresented Specific Sequences
Other potential sources…
Ribosomal
Contaminant
Notes: Ribosomal from (same as GC earlier, mouse total RNA)
file:///C:/Users/inglesfs/Downloads/SRR18752205_GSM6043804_Control_Eed_EPC._rep2_Mus_musculus_RNA-Seq_1_fastqc.html#M9
Ecoli from file:///C:/Users/inglesfs/Downloads/SRR11517364_GSM4471316_lung2_RNA_Homo_sapiens_RNA-Seq_1_val_1_fastqc.html#M9
(also see Ecoli in this sample in fastq screen, should be mouse)
Phage from Shcherbina_2020
file:///C:/Users/inglesfs/Downloads/SRR10347759_GSM4140578_MuSC_d0_Young_bulkATACseq_Rep1_Mus_musculus_ATAC-seq_1_val_1_fastqc.html#M9

## Slide 94: Overrepresented Specific Sequences
Which of these libraries would you expect to flag with overrepresented specific sequences?
Whole Genome Bisulfite Library
Amplicon Library
RNAseq Library
Notes: Amplicon
Sample 4135 lineage Cas9 4days Nextera amplicon
https://www.bioinformatics.babraham.ac.uk/sierra/sierra.pl/lane5716_AGGCAGAA_AAGGAGTA_E03_L001_R1_val_1_fastqc.html?action=send_file&lane_id=5716&path=%2Fdata%2Fprivate%2Fsierra%2Fdata%2F170802_M02293_0292_000000000-AU96R%2FUnaligned%2FProject_000000000-AU96R%2FSample_lane1%2Flane5716_AGGCAGAA_AAGGAGTA_E03_L001_R1_val_1_fastqc.html#M4
Also
Libraries focused on small RNAs
Long non coding RNAs
Ribosomal RNAs

## Slide 95: Overrepresented Specific Sequences
Which of these libraries would you expect to flag with overrepresented sequences?
Notes: Amplicon
Sample 4135 lineage Cas9 4days Nextera amplicon
https://www.bioinformatics.babraham.ac.uk/sierra/sierra.pl/lane5716_AGGCAGAA_AAGGAGTA_E03_L001_R1_val_1_fastqc.html?action=send_file&lane_id=5716&path=%2Fdata%2Fprivate%2Fsierra%2Fdata%2F170802_M02293_0292_000000000-AU96R%2FUnaligned%2FProject_000000000-AU96R%2FSample_lane1%2Flane5716_AGGCAGAA_AAGGAGTA_E03_L001_R1_val_1_fastqc.html#M4
Also
Libraries focused on small RNAs
Long non coding RNAs
Ribosomal RNAs

## Slide 96: Assessing Consistency

## Slide 97: Aggregated Statistics
Individual QC reports are useful but helpful to have a wider picture
Sample 1
  Aggregate and plot range of QC stats together
Sample 2
https://multiqc.info/modules/
Notes: Aggregate and plot range of QC stats together
Individual QC reports are useful but can be difficult to interpret without context
Help us spot local QC problems
We can aggregate and plot a range of QC statistics to make this easier
The simplest way to spot a local QC problem is that one sample doesn't look like the rest

## Slide 98
Sample1
Sample2
Sample3
Sample4
Sample5
Sample6
6 Samples, 24 files:
  Paired end
  Pre/post trimming

## Slide 99: Aggregated Mapping Stats
FastQ Screen
Identify local QC problems by spotting samples that behave differently
Notes: The simplest way to spot a local QC problem is that one sample doesn't look like the rest
Olivia?

## Slide 100: Putting QC into Practice

## Slide 101: Expectations and Observations are Key
Can you tell if these libraries are any good?
Notes: You can’t tell without the bigger picture, need the context of the library type / experiment
Also need to actually look at the underlying data
We also need the bigger picture, not just fastqc other stats about the library too
First one is a chip input (untrimmed)
Second one is RNA-seq
Third one is Repeat Amplicon Bisulphite

## Slide 102: QC In A Nut-Shell
Expectations
Observations
Critical Analysis
Understanding & Confidence
Good Science 

## Slide 104
Exercise: Assess the Quality of Public Sequencing Datasets
Fastq File
QC Metrics:
FastQC
Trimmed Fastq File
Aligned File
e.g. bam file
QC Metrics:
Aligner programme dependent QC stats
e.g. mapping statistics
QC Metrics:
FastQC
FastQ Screen
RNA-Seq
ATAC-Seq
ChIP-Seq
WGBS
Consider Expectations
Review Observations